## Slide 1
Local 5G DDoS Experimentation
& AI-Based Detection
Eryk Schiller, Leonardo Padial, Joachim Schmidt, Anna Padée
HEPIA / HESSO
PARTICIPANT CHALLENGE • 22 OCTOBER 2026 • ATHENS, GREECE
Generate → Capture → Classify → Mitigate → Share

## Slide 2
The challenge in five steps
6G-DALI × NATWORK | LOCAL CYBERSECURITY HACKATHON
02
01
RUN
Local isolated 5G testbed
02
CAPTURE
Record PCAP traffic
03
DETECT
Score with pretrained CNN
04
MITIGATE
Optional online protection
05
SHARE
Contribute to 6G-DALI
Everything runs on the participant’s own Linux laptop; no remote attack infrastructure.

## Slide 3
One repository • two working directories
6G-DALI × NATWORK | LOCAL CYBERSECURITY HACKATHON
03
git clone https://github.com/Hepia/cloudnet_hackathon.git
cd cloudnet_hackathon
infrastructure/
Docker Compose • Open5GS • UERANSIM
Traffic generator • PCAP collection
Run ./lab.sh here
ddos_cnn_xgb/
PCAP → HDF5 → 100-packet windows
Pretrained CNN • predictions
Run Python scripts here
Repository: github.com/Hepia/cloudnet_hackathon

## Slide 4
Network architecture — from infrastructure/README.md
6G-DALI × NATWORK | LOCAL CYBERSECURITY HACKATHON
04
Isolated Docker lab: clients and simulated UE reach services through a router; 5G user plane via gNB and UPF.
SERVERS • 10.10.1.0/24
ROUTER
CLIENTS • 10.10.2.0/24
5G CORE / RADIO
HTTP .10
MQTT .20
Video .30
iperf3 .40
Custom .50
router
10.10.1.1 / 10.10.2.1
HTTP client .10
MQTT client .20
Video client .30
UPF .100
Open5GS core
10.10.3.0/24
UERANSIM gNB
10.10.3.30
UE + custom-client
10.45.0.x via tunnel
Capture on router (server and client interfaces), optionally UPF and gNB. PCAP files → infrastructure/captures/

## Slide 5
Laptop readiness • prepare before the event
6G-DALI × NATWORK | LOCAL CYBERSECURITY HACKATHON
05
HOST
Native Linux x86_64 / amd64
DOCKER
Engine 26+ • Compose v2 • recent Buildx
KERNEL
/dev/net/tun • SCTP support • NET_ADMIN
SIZING
Plan for 4 CPU / 8 GB RAM / 15 GB free minimum
RECOMMENDED
8+ CPU cores • 16 GB RAM • 30 GB SSD free
NETWORK
Internet for initial build; isolated at runtime
Check for address conflicts: 10.10.1–4.0/24 and 10.45.0.0/16. Laptop sizing is an estimate, not a benchmark.

## Slide 6
Start the lab and capture PCAPs
6G-DALI × NATWORK | LOCAL CYBERSECURITY HACKATHON
06
cd infrastructure
./lab.sh up
./lab.sh status
./lab.sh test
./lab.sh pcap start
./lab.sh custom -s 10.10.1.0/24 -t 5 -d 10
./lab.sh pcap stats
./lab.sh pcap stop
ls captures/
Challenge scenario
Mirai-inspired traffic within isolated testbed networks only.
10.10.1.0/24 is the intended randomized destination range.
Check the provided custom generator implementation: the public README documents -s as a host and -d as per-request delay.

## Slide 7
PCAP collection points and baseline traffic
6G-DALI × NATWORK | LOCAL CYBERSECURITY HACKATHON
07
ROUTER
./lab.sh pcap start
Both server-side and client-side interfaces
UPF
./lab.sh pcap start upf
N3, N6 and ogstun / decapsulation
gNB
./lab.sh pcap start gnb
Radio and core network interfaces
Generate legitimate background traffic with the README’s HTTP, MQTT, RTP/video and iperf3 commands. Stop each capture point separately.

## Slide 8
Offline detection • three-command pipeline
6G-DALI × NATWORK | LOCAL CYBERSECURITY HACKATHON
08
cd ../ddos_cnn_xgb
python3 -m venv .venv
.venv/bin/python -m pip install numpy h5py tensorflow scapy scikit-learn
unzip best_run.zip -d best_run
mkdir -p pcaps tf_dataset
01 CONVERT
.venv/bin/python convert_pcap_to_h5.py
--input pcaps --output tf_dataset/pckt.h5
--packet-length 64 --target-ip 10.45.0.2 --ddos-name router
02 WINDOW
.venv/bin/python split_h5_into_windows.py
--input tf_dataset/pckt.h5 --output tf_dataset/masked.h5
--window 100 --packet-length 64
03 CLASSIFY
.venv/bin/python classify_h5.py
--input tf_dataset/masked.h5 --model-dir best_run/run_003
--output tf_dataset/predictions.h5

## Slide 9
Interpret results and validate assumptions
6G-DALI × NATWORK | LOCAL CYBERSECURITY HACKATHON
09
Packets flagged DDoS: fraction with CNN probability > 0.5
Windows flagged attack: fraction with > 50% packets flagged
Optional threshold: --threshold 0.8 (trade-off with missed attacks)
Classifier outputs: probabilities and 0/1 decisions in predictions.h5
Important: automatic ground-truth labels depend on BOTH PCAP filename substring and IP match; verify them before interpreting accuracy.

## Slide 10
Bonus: real-time defense • final deliverables
6G-DALI × NATWORK | LOCAL CYBERSECURITY HACKATHON
10
LIVE CAPTURE
Stream packet observations
INFERENCE
Apply 64-byte / 100-packet preprocessing
DECISION
Identify suspicious sources
MITIGATION
Block or isolate source inside the lab
Participant deliverables
Documented PCAP captures and scenario / capture-point metadata
CNN detection results with verified labels where possible
Optional live defense: latency, effectiveness, false positives
6G-DALI dataset contribution through the approved EDC workflow
Raw PCAP support is not confirmed by the integration guide; coordinate accepted submission format with organizers.

## Slide 11
Scale up — generate a reproducible dataset
6G-DALI × NATWORK | LOCAL CYBERSECURITY HACKATHON
11
cd infrastructure
./lab.sh up # patched lab (Mirai + uplink fix)
./lab.sh status # wait: UE 10.45.0.2, bot on :23
# capture benign + Mirai together, one pass:
../datasets/generate_final.sh big 15 60
# -> datasets/pcap_big/ (~15 GB, snaplen 128)
ls -lh ../datasets/pcap_big/
# alternatives:
# generate_m.sh · capture_attack.sh + capture_benign.sh
Realistic by design
Benign app mix (HTTP, MQTT, video, iperf3) and the Mirai SYN flood run together on the same uplink.
The attack share fluctuates per chunk but averages ~30% across the 15 GB capture.
The UERANSIM nr-ue uplink is patched (bounded queue) so the flood no longer wedges the UE tunnel.

## Slide 12
Train and evaluate the per-packet detector
6G-DALI × NATWORK | LOCAL CYBERSECURITY HACKATHON
12
cd ddos_cnn_xgb
python3 -m venv .venv
.venv/bin/python -m pip install tensorflow h5py numpy scikit-learn
# one command does compose + train + compare:
./run_final_pipeline.sh ../datasets/pcap_big bigrun
01 COMPOSE
.venv/bin/python build_mixed_windows.py
-i ../datasets/pcap_big -o bigrun/mixed_masked.h5
-w 100 -p 64 --attack-frac 0.30 (fluctuating, address-randomized)
02 TRAIN
.venv/bin/python train_model.py --arch perpacket --loss bce
-i bigrun/mixed_masked.h5 -o bigrun/perpacket
--train-cap 150000 --epochs 8 (per-packet head, ~38k params)
03 COMPARE
.venv/bin/python evaluate_compare.py --csv bigrun/comparison.csv
-m shipped best_run/run_003 -m perpacket bigrun/perpacket
--eval-cap 60000 (same held-out split for every model)

## Slide 13
Result — per-packet CNN meets the NATWORK KPIs
6G-DALI × NATWORK | LOCAL CYBERSECURITY HACKATHON
13
Shipped CNN (global-window head): FP 55.7% · FN 36.7% — far above the 1% KPI
Same architecture retrained on the new data: FP 38.0% · FN 62.0% — still fails
New per-packet CNN: FP 0.0001% (3 / 4.2M) · FN 0.009% (162 / 1.8M) — PASS
Same 100-packet window I/O; the per-packet head is ~17× smaller (38k vs 671k params)
NATWORK KPIs met: false positives < 1% and false negatives < 1%, by three orders of magnitude — on real interleaved traffic with randomized addresses. Packaged as best_run_perpacket.zip.